## Slide 1: Rotary Centering Scan
Gulden Othman
8 March 2021

## Slide 2: Overview
Making a plan for rotary centering scans to help find the uncertainty in rotary angle position

## Slide 3: 72 Degree rotation
Rotation
Collimator
Direction of linear travel
Source arm
Taken from ./topview.pptx
We should use 72.0 deg as the “center point” for this scan

## Slide 4
(12.52 mm)/2
Linear travel
Rotation
6.5 mm
To scale
(S = 2 mm if we want a spot every 2 mm)
Determining the angle, , that needs to be traversed for rotary centering scans
r
Rotary motor at -72.08 deg
For r = 12 mm:
`
= beam spot position
9 mm

## Slide 5: Proposal
“center” point for this scan is rotary = -72.08 deg
Upper limit: 72.08 + theta/2 + 2*delta_theta = 119.6 -> 120 deg
Lower limit: 72.08 – theta/2 – 2*delta = 24.5 deg -> 24 deg
Try to get scan every ~2 mm arc length -> ~ d_theta = 10 deg
Final proposal: -24 deg to -124 deg in 10 deg increments
  11 scan positions
  I estimate about 8 hours of lab time with 30 min run + 15 min in between to move motors

## Slide 6: Other notes
Spot should start overlapping with front-end at rotary = -44.5 deg and overlap until rotary = -100 deg

## Slide 9: Moving source motor instead of linear
To get spot at 12 mm radius with the source centered above the p+ contact (ie linear motor centered) should rotate to:
  rotate collimator to: 28.61 deg
  theta_rot = 28.61 deg corresponds to theta_det = 61.39
For simplicity:
  Rotate source motor to 29 deg -> theta_det = 61 deg